## Slide 1
HARDWARE SETUP
main control
ready
in progress
MAIN CONTROL BOARD
peripherals
SENSING - ACC
MAIN CONTROL
  STM32H743IIT6
  480MHz
RAM:
  SRAM: 1 Mb (built-in)
  SDRAM: 32 Mb
ROM:
  FLASH: 2 Mb (built-in)
  QSPI FLASH 8 Mb
  NAND FLASH Slot
TF Card
  Up to 32 GB
IO:
  97 pins
  Type-C
  1 rst button; 1 boot button
  SWD Debug
  Serial Communication
LED
  1 power indication
  1 user programmable
COMMUNICATION
INTERFACING
LOW POWER ACC
12 bit
idle - 270nA/ sensing – 3uA
HIGH RESOLTUION ACC
20 bit
idle – 21uA / sensing – 150uA
ADXL362
ADXL355
DHT11
ENV SENSING
temperature
relative humidity
WIFI
ESP8266
BT
HC-05
CELLULAR
SIM-7600
OLED Scree
0.96 inch
PERIPHERALS
SENSING - VISION
OV5640
VISUAL SENSING
resolution: 2592x1944
idle – 20uA/ sensing – 140mA

## Slide 2
SOFTWARE FRAMEWORK
SOFTWARE ARCHITECTURE
FEATURES
APPLICATION
LAYER
MIDDLEWARE
LAYER
DRIVER
LAYER
HARDWARE
LAYER
USER DRIVERS
FATFS
RTOS
X-CUBE-AI
APPLICATION-SPECIFIC CODE
MAIN CONTROL
PERIPHERALS
STM32 HAL (Hardware Abstraction Layer)
INTERFACE
  LED
  Serial Communication (UART)
EDGE COMPUTING RELATED
  External RAM 32 Mb Driver (SDRAM using FMC)
  Memory Management Driver for External RAM
  CMSIS-DSP for Digital Signal Processing
STORAGE AND FILE MANAGEMENT
  External Storage Driver (SD Card using SDMMC)
  File System - FATFS
UNDER DEVELOPMENT
  FreeRTOS
  Drivers for Peripherals
    Sensing (DHT11, ADXL362&255, OV5640)
    Communication (ESP8266, HC-05, SIM-7600)
    Interfacing (OLED)
EDGE INTELLIGENCE
  CMSIS-NN
  X-CUBE-AI