## Slide 1
Front End
Edge
Back End
Cloud
Sensing
Storage
Computation
Communication
Internet
Coordination
Computation
Storage
Analysis
Interfacing

## Slide 2
MAIN CONTROL
SENSING
COMMUNICATION
INTERFACING
Microcontroller Unit
STM32H743IIT
480 MHz
Random Access Memory
SRAM: 1 MB (built-in)
SDRAM: 32 MB (ext.)
WINBOND W9825G6KH-6I
Read Only Memory
FLASH: 2 MB (built-in)
QSPI FLASH: 8 MB (ext.)
WINBOND W25Q64
TF Card
Up to 32 GB
LED
1 power indication
1 programmable
Button
1 boot; 1 reset
IO
PIN: 2x2x28, 2.54 mm
Type-C; SWD; Serial
Acceleration
Low Resolution Accelerometer
12 bit
idle - 270nA/ sensing – 3uA
ADXL362
High Resolution Accelerometer
20 bit
idle – 21uA / sensing – 150uA
ADXL355
Temperature & Humidity
DHT11
Environment Sensing
temperature
relative humidity
OV5640
Camera
Visual Sensing
resolution: 2592x1944
idle – 20uA/ sensing – 140mA
OLED Display
1.3 inch
CH1116
Screen
Near Field Communication
HC-05
HC-05
Blue Tooth
Internet Connection
ESP8266
IEEE 802.11 B/G/N
ESP-01S
WIFI
Internet Connection
SIM-7600
SIM-7600
4G Cellular Network
Main Control
Sensing
Communication
Interfacing

## Slide 3
PHYSICAL
LAYER
Main
Control
Sensing Components
Communication Components
Interfacing Components
STM32 HAL (Hardware Abstraction Layer)
STM32 HAL
User Customized Drivers
DRIVER
LAYER
APPLICATION
LAYER
Application Specific Code
MIDDLEWARE
LAYER
File System
FATFS
Real-Time Operating System
FreeRTOS
AI Deployment
X-CUBE-AI
Digital Signal Processing
CMSIS - DSP
Neural Network Computing
CMSIS - NN
Edge Intelligence Library for SHM Applications
TinySHM
TinySHM Math
TinySHM DSP
TinySHM Network
TinySHM File
TinySHM AI
TinySHM …

## Slide 6
MCU - STM32H743IIT6
32 MB SDRAM
W9825G6KH-6I
LED – BOOT Status
LED – Power Status
LED –
Programmable
USB-Type C
Buttons – Reset / Boot
Debug
Serial Communication
PIN
TF Card Slot
PIN
Front View
Back View
8 MB QSPI FLASH
W25Q64